## Slide 1
CSA07 • NUMERICAL-BASED MCQ
UNIT 1 Questions 16–20
Detailed step-by-step calculations
Formulas • Substitution • Final answers
Prepared from the uploaded CSA07 numerical MCQ PDF

## Slide 2
What these questions cover
Q16–20
Five short problems on protocol overhead and payload size
Q16
OSI layer overhead
500 B message + 7 × 20 B
Q17
Overhead percentage
4 layers × 10 B on a 1000 B message
Q18
Application payload
1500 B frame − IP/TCP headers
Q19
Overhead percentage
40 B headers added to an 800 B message
Q20
Maximum TCP MSS
MTU − IP header − TCP header
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
2

## Slide 3
Q16 • Total size after OSI overhead
Q16
Question: A 500 B message gains 20 B at each of the 7 OSI layers. What is the total size?
Step-by-step calculation
1. Message size = 500 B
2. Total overhead = number of layers × overhead per layer
= 7 × 20 B = 140 B
3. Total size = message size + overhead
= 500 B + 140 B = 640 B
Final answer
500 + (7 × 20)
= 500 + 140
= 640 B
Correct option: B
Remember: total transmitted size = original message + all layer headers.
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
3

## Slide 4
Q17 • Calculate overhead percentage
Q17
Question: Four layers each add 10 B to a 1000 B message. Find the overhead percentage.
Step-by-step calculation
1. Total overhead = 4 × 10 B = 40 B
2. Message size = 1000 B
3. Overhead percentage = (overhead ÷ message size) × 100
= (40 ÷ 1000) × 100
= 0.04 × 100 = 4%
Final answer
Overhead = 40 B
Percentage = 4%
Correct option: B
Note: the PDF's explanation also corrects the answer to option B.
Use the original message size as the denominator for this question's stated method.
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
4

## Slide 5
Q18 • Maximum application payload
Q18
Question: A 1500 B Ethernet frame has a 20 B IP header and a 20 B TCP header. Find the maximum application payload.
Step-by-step calculation
1. Total IP + TCP header = 20 B + 20 B = 40 B
2. Frame size available = 1500 B
3. Application payload = frame size − headers
= 1500 B − 40 B
= 1460 B
Final answer
Payload = 1500 − (20 + 20)
= 1500 − 40
= 1460 B
Correct option: A
The headers occupy 40 B, leaving 1460 B for application data.
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
5

## Slide 6
Q19 • Overhead as a percentage of total
Q19
Question: An 800 B HTTP message has 40 B of TCP + IP overhead. Find the overhead percentage.
Step-by-step calculation
1. HTTP message = 800 B
2. TCP + IP overhead = 40 B
3. Total transmitted size = 800 B + 40 B = 840 B
4. Overhead percentage = (overhead ÷ total size) × 100
= (40 ÷ 840) × 100 ≈ 4.76% ≈ 4.8%
Final answer
40 ÷ 840 × 100
≈ 4.76%
≈ 4.8%
Correct option: A
Here, the denominator is total transmitted size: 800 B data + 40 B overhead.
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
6

## Slide 7
Q20 • Maximum TCP MSS
Q20
Question: MTU = 1500 B, IP header = 20 B, and TCP header = 20 B. Find the maximum segment size (MSS).
Step-by-step calculation
1. MTU = 1500 B
2. Total headers = IP header + TCP header
= 20 B + 20 B = 40 B
3. MSS = MTU − total headers
= 1500 B − 40 B = 1460 B
Final answer
MSS = 1500 − 20 − 20
= 1460 B
Correct option: B
MSS is the TCP data payload size; it excludes the IP and TCP headers.
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
7

## Slide 8
Quick revision • Answers at a glance
RECAP
Q.No.
Formula
Result
Option
Q16
500 + (7 × 20)
640 B
B
Q17
(4 × 10 ÷ 1000) × 100
4%
B
Q18
1500 − 20 − 20
1460 B
A
Q19
(40 ÷ 840) × 100
≈ 4.8%
A
Q20
1500 − 20 − 20
1460 B
B
Key formulas: Total size = data + overhead | MSS = MTU − IP header − TCP header
CSA07 • UNIT 1 • NUMERICAL MCQ SOLUTIONS
8