## Slide 1
1 / 5
Q16. ARQ retransmission probability
Link BER = 10⁻⁵ and frame size = 1000 bits. What is the probability that a frame contains an error (and may need retransmission)?
A. 0.01
B. 0.02
C. 0.05
D. 0.10
Correct answer: A — 0.01 (approximately)
P(error) = 1 − (1 − BER)ⁿ
= 1 − (1 − 10⁻⁵)¹⁰⁰⁰
≈ 0.00995 ≈ 0.01 (about 1%).
Computer Networks • Answers and worked explanations

## Slide 2
2 / 5
Q17. Stop-and-Wait throughput
RTT = 50 ms, frame size = 1250 bytes, and link rate = 1 Mbps. Find the approximate throughput.
A. 0.2 Mbps
B. 0.4 Mbps
C. 0.8 Mbps
D. 1 Mbps
Correct answer: A — approximately 0.2 Mbps
Frame transmission time = (1250 × 8) / 1,000,000 = 10 ms.
Cycle time ≈ RTT + transmission time = 50 + 10 = 60 ms.
Throughput ≈ 10,000 bits / 0.06 s = 0.167 Mbps ≈ 0.2 Mbps.
Computer Networks • Answers and worked explanations

## Slide 3
3 / 5
Q18. Go-Back-N maximum window size
What is the maximum sender window size for Go-Back-N (GBN) when sequence numbers use k bits?
A. 2ᵏ
B. 2ᵏ − 1
C. 2(k − 1)
D. k
Correct answer: B — 2ᵏ − 1
With k-bit sequence numbers, there are 2ᵏ distinct sequence numbers.
GBN reserves one sequence-number value to distinguish new frames from old ones, so the maximum window is 2ᵏ − 1.
Computer Networks • Answers and worked explanations

## Slide 4
4 / 5
Q19. Selective Repeat maximum window size
What is the maximum window size for Selective Repeat (SR) when sequence numbers use k bits?
A. 2⁽ᵏ⁻¹⁾
B. 2ᵏ
C. k
D. 2ᵏ − 1
Correct answer: A — 2⁽ᵏ⁻¹⁾
There are 2ᵏ sequence numbers. To prevent ambiguity between old and new frames after sequence numbers wrap around, the SR window can be at most half the sequence-number space: Wmax = 2ᵏ / 2 = 2⁽ᵏ⁻¹⁾.
Computer Networks • Answers and worked explanations

## Slide 5
5 / 5
Q20. Stop-and-Wait efficiency
RTT = 100 ms, frame size = 1000 bytes, and link rate = 10 Mbps. Find Stop-and-Wait efficiency.
A. 0.08
B. 0.16
C. 0.32
D. 0.64
Calculated efficiency: ≈ 0.008 (0.8%) — none of the listed options matches
Transmission time = (1000 × 8) / 10,000,000 = 0.8 ms.
Ignoring ACK transmission time, efficiency ≈ Ttx / (RTT + Ttx)
= 0.8 / 100.8 ≈ 0.00794 = 0.794%.
Note: the source image marks A, but 0.08 means 8%, which is inconsistent with this calculation.
Computer Networks • Answers and worked explanations